|  | Member of the MacTaggart Scott Group MACSCOTT BOND LTD Engineering with Hydraulics Aberdeen Division UNIT 2, BLACKNESS ROAD ALTENS INDUSTRIAL ESTATE ABERDEEN AB12 3LH Tel: 01224 873113 Fax: 01224 877700 |
| --- | --- |

OPERATING INSTRUCTIONS  FOR PRESSURE TEST AND FLUSHING UNIT MSB 201

| Prior to use of this Equipment, these instructions should be Read , Understood and its Operation Carried out by Designated “Competent “ Personnel |
| --- |
| NO: | INSTRUCTIONS : |
|  | FLUSHING PUMP : |
| 1. | Fill reservoir with fluid. (Please ensure there is sufficient fluid in the reservoir to access the Float Switch) |
| 2. | Ensure Suction Ball Valve is open on underside of Reservoir. |
| 3. | Connect to Electrical Supply. |
| 4. | Ensure Outlet and Return Ball Valves are closed and By-pass Ball Valve is open on |
|  | Flushing System |
| 5. | Jog Motor and check Motor rotation. ACW from fan end |
| 6. | Connect to System. (Supply and Return) |
| 7. | Open Supply and Return Ball Valves |
| 8. | Close By-pass Ball Valve. |
| 9. | Flow Can be adjusted on pumpo front face (1/4” Allen Bolt). In to reduce flow. |
| 10. | The pump is Pressure Compensated which has been factory set at 207 bar |
|  | Pressure Relief Valve is set at 220 bar - Do Not Adjust |
| 11. | Samples can be taken from Return Valve Sample Point |
|  | AIR OPERATED PUMP : |
| 12. | The 400 bar and 1000 bar Systems can be set by using the Air Regulator |
| 13. | The 400 bar System has a 20 Litre Bladder Accumulator which can be isolated from |
|  | the System at the Safety Block fitted to the Accumulator |
| 14. | The Pressure Relief Valves are set at 420 bar and 1040 bar |
| . | Do Not Adjust |
| NOTE : Customers are advised to flush the Unit through with their own system fluid in order to eliminate the danger of system contamination due to unforseen ciscumstances and / or in the event of wrongly supplied fluid relating to fluid type. |