|  | Member of the MacTaggart Scott Group MACSCOTT BOND LTD Engineering with Hydraulics Aberdeen Division UNIT 2, BLACKNESS ROAD ALTENS INDUSTRIAL ESTATE ABERDEEN AB12 3LH Tel: 01224 873113 Fax: 01224 877700 |
| --- | --- |

OPERATING INSTRUCTIONS  FOR ELECTRIC DRIVEN POWER UNIT  SERIAL NO. MSB 120

| Prior to use of this Equipment, these instructions should be Read , Understood and its Operation Carried out by Designated “Competent “ Personnel |
| --- |
| NO: | INSTRUCTIONS: |
| 1 | Fill Tank. (Please ensure there is sufficient fluid in tank to cover the Float Switch) |
| 2 | Ensure Suction Valve on Tank is open. |
| 3 | Connect Electrical Supply. |
| 4 | Ensure No Load start is in “Offload” position. |
| 5 | Back off Pump pressure control. |
| 6 | Directional Control Valve in neutral position. |
| 7 | Close Ball Valves on A and B Lines. |
| 8 | Ensure Sample Valves are closed. |
| 9 | Switch Pump on and off to check rotation (C.W.) |
| 10. | Start Pump and run Off Load for 1 minute. |
| 11. | Put Pump on load and set Pump Pressure Control to required pressure. |
| 12. | Open Ball Valve on A and B lines after connection to system. |
| 13. | Position Directional Control Valve as required. i.e. Push forward for fluid from rear connection ‘B’ Pull for ‘A’. |
| 14. | Check flow and adjust as required by screwing “In” Allen bolt on front face of pump to decrease and out to increase. |
| 15. | Put Pump Off Load prior to switching Off. |
| 16. | Monitor Filter Indicators during use. |
| NOTE : Customers are advised to flush the Unit through with their own system fluid in order to eliminate the danger of system contamination due to unforseen ciscumstances and / or in the event of wrongly supplied fluid relating to fluid type. |